## Slide 1: ENGI 301 Pencil-Programmable Music Box Proposal
10/3/2020
Michael Tang

## Slide 2: Background Information
Idea: Making an electronic version of the “punchcard music box”
  Punchcard music box: https://youtu.be/qdj8kpP4fGY?t=19
    Basically, you can program this music box by hole punching the tune you want into a piece of paper, and then feeding the paper into the music box through a crank – music is made when strings inside the box get caught on the holes and get plucked
  I want to do the same thing, but instead of strings getting plucked, a buzzer will play different pitches, and instead of punching holes, the user can fill in what notes they want with a pencil
    Since graphite conducts, I want it to work so that when the paper is fed through, the “notes” drawn in with a pencil act like a switch and close the circuit and trigger a certain sound to be played through a buzzer
    In addition to a buzzer, I want to have a volume control, and an LCD screen that shows the current tempo at which the user is cranking the paper through the device
Existing resources online for this project:
  https://www.hackster.io/nickericlester/ir-breakbeam-candy-dispenser-with-zelda-music-c76e65
    Project has code mapping what frequencies are needed to get each note
  https://www.reddit.com/r/DIY/comments/2xsrgd/how_to_build_a_programmable_music_box/
    Someone else had exact same idea here – was not actually implemented, but comments offer a few alternative suggestions on implementation (ie. Using capacitive sensing to sense each pencil mark instead of treating it as a switch, or detecting presence of pencil mark using a photodiode instead)
  Will use your library for the 4-digit LCD display

## Slide 3: System Block Diagram
Create a System Block Diagram
  Label interfaces / pins
  Components (part numbers if possible)
PocketBeagle
PWM1
PWM2
PWM3
Speaker 1
Speaker 2
Speaker 3
12x “Graphite Switches”
12x GPIO_IN
AIN 3.3V
4-Digit 7-Segment Display
I2C1
Potentiometer
Create a System Block Diagram
  Label interfaces / pins
  Components (part numbers if possible)

## Slide 4: Power Block Diagram
Create a Power Block Diagram
  Label voltages / currents of components
PocketBeagle
PWM
PWM
PWM
Speaker 1
Speaker 2
Speaker 3
12x “Graphite Switches”
SYS VOUT
SYS 3.3V
4-Digit 7-Segment Display
SYS 3.3V
Potentiometer
3.3V, current varies
3.3V, 20 mA
5V, current unknown
3.3V, 140 mA
3.3V, 140 mA
3.3V, 140 mA

## Slide 5: Components / Budget
Component | Need to Buy | Cost
Speaker - https://www.adafruit.com/product/1898 | 3 | 1.85 * 3 = $5.55
Continuous Rotation Servo - https://www.sparkfun.com/products/10189 | 1 | $11.95